## Slide 1
Some questions from Lecture 1 (Berg):
1) Why are the dots on the “Diagnostics in focal plane of Spectrometer” so evenly spaced?
2) What is the real world example of measuring emittance?
3) Describe the focal plane diagnostics of the spectrometer in more detail
4) l doesn't appear to have a dependence on anything. Can you clarify how l(t) transforms? How exactly is l define?
5) Can you show a (x|a)!=0 case
6) Why is sigma matrix symmetric? What is definition of sigma_21? How do we create the 6×6 ellipse matrix?
7) How does the x-Theta measurement setup look like (measure orientation of ellipse)
8) Definition of Louisville Theorem
9) How do we define the central ray?
10) R11, R12, R21, R22 - can more than one be zero?

## Slide 2: Question 1)
Why are the dots on the “Diagnostics in focal plane of Spectrometer” so evenly spaced?
Answer: This is an artifact of poor binning, see next slide upper scatter plot Theta vs. x1 position.
This was corrected in the lower scatter plot on the next slide

## Slide 3: Diagnostics in focal plane of spectrometer
Typical in focal plane of
Modern Spectrometers:
Two position sensitive
Detectors:
Horizontal: X1, X2
Vertical: Y1, Y2
Fast plastic scintillators:
Particle identification
Time-of-Flight
Measurement with IUCF K600
Spectrometer illustrates from top
to bottom: focus near, down-
stream and upstream of
X1 detector, respectively
IUCF, K600 Spectrometer

## Slide 4: Question 2)
What is the real world example of measuring emittance?
Answer: A real world measurement would have been done in an existing device. Since we do not have such
we use “calculated data” for the exercise.

## Slide 5: Question 3)
Describe the focal plane diagnostics of the spectrometer in more detail
Answer: See next slide of K600 with focal plane detector system. The see slide 3
with x-Theta plot for detailed explanation.

## Slide 6: K600 Spectrometer
Bending radius r0 = 2.0 m
Bmax = 1.7 T
Gap = 5 cm (D 1), 6cm (D2)
Weight = ~ 30 tons (D1)
~ 45 tons (D2)
Medium Dispersion: B(D1)= B(D2)
Resolving power: p/Dp = 20000
Dispersion = 12 cm/% ( = 12 m )
Magnification Mx = 0.41
Large range: Emin /Emax = 1.14
The K600 is shown in
0o Transmission mode
High Dispersion Plane
B(D1) > B(D2)
Kinematic correction: K coil
Hexapole correction: H coil
IUCF K600,decommissioned In 1999, now in WS line RCNP
iThemba Labs K600,
South Africa in use
(x|f2)
(x|Q2)
(x|Q)
3 dispersion modes
(low,medium,high)
set by D2/D1 ratio
low
medium
high

## Slide 7: Question 4)
l doesn't appear to have a dependence
on anything. Can you clarify how l(t)
transforms? How exactly is l define?
Answer: l(t) = R651*x_0+R52*Theta_0+l_0+R5*delta_0

## Slide 8: Question 5)
Can you show a (x|a)!=0 case?
Answer: See slide 3

## Slide 9: Question 6)
Ellipse in matrix form, see TRANSPORT MANUAL p. 169
To make an ellipse the sigma matrix has to fulfill the following conditions
Real
Positive definite: det(sigma) > 0 (Note: Area of ellipse is A = Pi*epsilon)
Symmetric (sigma(n) = sigma(m) for m not equal n
Why is sigma matrix symmetric? What is definition of sigma_21? How do we create the 6×6 ellipse matrix?
Answers: See this and next 2 slides

## Slide 10: sigma 21 = sigma 12 represents the tilt of the ellipse and is in the ellipse drawing via r12

## Slide 11: Symmetric sigma of 6 dimensional ellipsoid

## Slide 12: Question 7)
How does the x-Theta measurement setup look like (measure orientation of ellipse)
Answer: See slide 6 of K600 with focal plane detector system. The see slide 3
with x-Theta plot for detailed explanation. Caveat. Beam intensity may be too high
for detector system. Use attenuated (faint) beam.

## Slide 13: Question 8)
Definition of Louiville Theorem
Answer: Liouville’s Theorem states that “The density of states in an ensemble of many identical states
with different initial conditions is constant along every trajectory in phase space”.
Applied to our case is means that the emittance epsilon (area/volume of the ellipse) does not change
Under conservative forces. Conservative forces F are forces where the work (integral F dl) is independent
of the path.

## Slide 14: Question 9)
How do we define the central ray?
Answer: The Central Ray is a fictitious line through the magnetic center of quadrupoles. For passage through
dipoles see drawing below, TRANSPORT manual p. 136

## Slide 15: Question 10)
R11, R12, R21, R22 - can more than one be zero?
Answer: If R12=0 it follows that R11 = 1/R22. I do not think R21 = 0 has a physical meaning. But I do not have a proof. Note that this is the Transfer matrix, not the symmetric matrix that defines an ellipse. So R is not necessarily symmetric.