## Monitoring Beam Power
##### What Is Beam Power?
- Beam Power is a measurement of how much beam we're sending, it's measured in Watts (W) and can be found using the following formula
- (Current/Charge) * Mass * Energy * Stripper Efficiency (using latex for this and link following references)
  - We measure the current from either Farday Cups or BPMs, the charged beam induces current in the cups idk how i guess just attracts all neg to the surface? BPMs no clue
  - Mass is just dependent on the isotope we're sending
  - Energy increases as the beam is accelerated by more cavities, so it will change depending on the destination,
  - Stripper Efficiency is the amount of beam that passes through the Lithium Stripper and Charge Selector in FS1, if the Stripper is turned off then we would have 100% efficiency as all beam would pass through, if it were tuned incorrectly and didn't allow any beam to pass through, then it would be 0%. Another way to think of it is what percent of the initial beam that makes it to the LINAC is the desired charge, if we want a charge state that's 70% of the beam then we'd want 70% efficiency, if we want an additional charge state that's 15% of teh beam then this goes to 85%.
#### Limiting Beam Power
Link to info page
## Actually monitoring it, first section could be another page
#### Knowing the Limit
- check teh ose
- check Steiner tool
#### Reading the Power
on the display