## Slide 1: Simulation of a Low-Background Proton Detector for Studying Low-Energy Resonances Relevant in Thermonuclear Reactions D. Perez-Loureiro1, C. Wrede1,2 1National Superconducting Cyclotron Laboratory, Michigan State University, East Lansing, Michigan, USA 2Department of Physics and Astronomy, Michigan State University, East Lansing, Michigan, USA
Proposed Detector
Requirements
Ability to detect b-delayed protons and a-particles with kinetic
energies as low as possible.
High detection efficiency.
Energy resolution below 8% FWHM at low energies.
Ability to distinguish b-p and b-p-g (using together Ge arrays)
No beta-background above 200 keV.
REFERENCES:
[1] J. Jose et al., The Astrophysical Journal 494,680,(1998)
[2] Y. Giomataris et al. Nucl. Instr. and Meth. A, 376 (1996), 29
[3] E. Pollacco et al., Nucl. Instrum. Methods. Phys. Res., Sect. A 723, 102 (2013)
[4] J. Pancin et al., Nucl. Instrum. Methods. Phys. Res., Sect. A 735, 532 (2014)
The Authors want to thank E. Pollacco and the AstroBox
Collaboration for their valuable help and fruitful discussions.
Credit for the Nova Artistic Picture: Hardy and PPARC.
Credit for the Nova Nucleosynthesis calculation: J. Jose et al.
ACKNOWLEDGEMENTS:
Introduction
Simulation
Micro Pattern Gaseous Detectors (MPGDs)
Drift Region
Decay products from implanted nuclei ionize the gas along their trajectories.
Secondary electrons produced drift to anode pads under an applied field.
Amplification Region
Avalanche multiplication due to high electric field
Amplitude of signal induced in readout pads proportional to energy
Fast timing, robust, cost effective, good energy resolution
Results
Next Steps
Based on GEANT4 and ROOT packages.
Two stage simulation:
Gas interaction of implanted and decay products
Simulation of detector response in a semi-analytical approach.
  Define final geometry of the detector as well as pad plane.
  Design of a position sensitive pad plane for adding multi-particle identification capabilities.
  Realistic GARFIELD simulations of the field cage.
  Add gamma detectors to simulation.
  Test with MicroMEGAS prototypes.
  Commissioning experiment with 23Al beam.
Simulation of drift, amplification and digitization of MPGDs
  Calculation of primary electrons from energy deposited at each interaction step with Poisson fluctuation.
  Randomization of the final position at the anode according to transversal diffusion coefficients for each of the electrons produced (charge spread).
  Gain fluctuations calculated for each electron using the Polya distribution.
  Charge collected on pads is the sum of all the electrons produced.
  Charge thresholds applied .
  Event stored in a ROOT file.
Classical novae occur in close binary star systems containing an ordinary star and a white dwarf (WD). Gravity attracts some hydrogen-rich material from the ordinary star that accumulates on the surface of the WD. After sufficient time, the temperature and pressure at the base of the accumulating material becomes large enough for thermonuclear reactions to occur. These reactions produce an increase in the temperature and pressure, which in turn leads to a runaway and finally an explosion.
Artist impression of a dwarf star ‘feeding’ on donor star.
Main nuclear flow in terms of reaction fluxes at peak temperature, for a nova explosion [1].
Energy generation and nucleosynthesis in novae depend on nuclear reaction rates, mostly resonant radiative proton captures.
Due to unavailability of intense radioactive ion beams of several species, resonances have to be studied by indirect methods, like beta-delayed particle emission.
Problem
Resonance energies are close to the proton separation energy (Sp), therefore kinetic energies are very low and they overlap with the beta background. In addition, proton emission competes with gamma decay, and thus sometimes has a very low probability due to Coulomb and centrifugal barriers.
AY
AX
A-1Z+p
E
b2
b1
g1
g2
g3
g4
g5
p1
p2
p3
Sp
Example of the decay scheme of beta-delayed proton emission
.
HV1
HV2
E1
100 V/cm
E2
50 kV/cm
10 cm
100 mm
Cathode
MicroMesh
Drift Region
Amplification Region
b
p
e-
e-
e-
e-
e-
ne
Readout Electronics
Principle of Operation of the proton detector based on MPGDs
Proposed detector and read out pads geometry.
120 mm
180 mm
b3
60 mm
Screenshot of the GEANT4 simulation
Example of a simulated decay of 23Al(b p)22Na event and its projected pad response
b
p
Full energy proton efficiency versus kinetic energy.
Simulated spectrum of the central pad of the proton detector for the beta-decay of 23Al.
(xi,yi,zi,ti,DEi)
Protons+Betas
Betas
197 keV
222 keV
255 keV
554 keV
828 keV
150 keV
<sv>: Reaction rate, ER: Resonance energy, T: Temperature, wg: Resonance strength, Ji: Spins, Gi: Partial widths, G: Total resonance width.
CONTACT INFORMATION:
email: perez-loureiro@nscl.msu.edu