## Slide 1: Conceptual Design and Simulation of a Proton Detector for studying low-energy resonances relevant in thermonuclear reactions
David Perez-Loureiro
NSCL, Michigan State University
Collaborators: C. Wrede, E. Pollacco and the AstroBox collaboration

## Slide 2: Outline
Motivation
Conceptual Design
MicroMEGAS Detectors
Detector Simulations
Summary and Outlook

## Slide 3: Motivation
White dwarf (Novae) or neutron star (type I X-ray burster) accreting H from binary companion
Temperature increases without expansion
Hot CNO cycle ignites thermonuclear runaway at surface
Temperatures up to 0.4 GK (Novae) and 2 GK (type I X-ray burst)
Nova Cygni 1992 (in 1994) NASA, ESA, HST
Credit: David A. Hardy/http://www.astroart.org & PPARC
Notes: X-ray bursters are explosions on the surface of neutron stars which accrete material from a companion star in a stellar binary system. They are characterised by intense short-lived bursts of X-rays. A key question about such explosions is the trigger for the break-out from the hot-CNO cycle into the rp-process.
There are a number of reactions of interest in terms of the break-out from the hot-CNO cycle. These include 15O(α,γ), 14O(α,p) and 18Ne(α,p). Ideally, we would study these reactions directly and obtain astrophysical reaction rates for them for the complete temperature regime of interest. In practice, this is extremely challenging as each of the nuclei are short-lived radioactive species. Such nuclei can be produced as accelerated radioactive beams at facilities such as Oak Ridge National Laboratory in the US, REX-ISOLDE in CERN, ISAC in Vancouver and CRIB in Japan. It has not been possible, however, to obtain these beams with sufficient intensity to make direct measurements with a useful precision, or at energies corresponding to sufficiently low temperatures.

## Slide 4: Nucleosynthesis
Proton captures and b-decays
Nucleosynthesis in novae and X-ray bursts depends on thermonuclear reaction rates
15O(a,g)19Ne is one of the two routes to break out CNO cycles and trigger rp-process in X-ray bursts
30P(p,g)31S reaction is a potential bottleneck for rp-process in ONe novae (t1/2=2.5 min)
Dominated by resonant capture
Can’t be measured directly because of low intensities available
Indirect methods
3
4
5
6
7
8
9
10
11
12
13
14
C (6)
N (7)
O (8)
F (9)
Ne (10)
Na (11)
Mg (12)
3a process
15O(a,g)19Ne
Neutron Number
Proton Number
HOT CNO cycle

## Slide 5: Indirect measurements
b-delayed particle and g emission
Excited stated of the nucleus of interest populated in beta-decay of precursor
Need to measure Er,Gg,Gp and Jr
X
b
g
Y
Z+p
p
E

## Slide 6: Detector requirements
Ability to detect b-delayed ps and as as low in energy as possible with high efficiencies because Gparticle << Gg at low energies due to Coulomb and centrifugal barriers
Beta energy deposition: can cause background and summing
Need to distinguish b-p from b-p-g
Multi-charged-particle emission
Want detector chamber to fit inside cylindrically-symmetric SeGA array, which has an inner diameter of 18cm
Want sensitivity to protons and alphas below 200 keV (ideally beta background stops at 150 keV)
SeGA
31Cl b-delayed gamma emission measured at NSCL (analysis ongoing)
20Mg b decay experiment accepted by PAC to investigate 15O(a,g)19Ne

## Slide 7: MicroMEGAS Detectors
Drift Region
  Particles ionize the gas along their trajectories
  Electrons drift to anode pads under an applied field (~100 V/cm)
Amplification Region
  Avalanche multiplication
  Signal induced in readout pads
  Fast timing, robust, cost effective, good energy resolution
HV1
HV2
E1
100 V/cm
E2
50 kV/cm
10 cm
100 mm
Cathode
MicroMesh
Drift Region
Amplification Region
Readout Pad
b
ne
p
e-
e-
e-
e-
Y. Giomataris et al. Nucl. Instr. and Meth. A, 376 (1996), p. 29
e-

## Slide 8: AstroBox detector
E. Pollacco et al. Nucl. Instr. and Meth. A, 723 (2013), p. 102
Similar detector already used at Texas A&M University Cyclotron
Successful operation with 23Al beam
Same technology based on MGPDs

## Slide 9: NSCL ProtonDetector Simulation
Based on Geant 4.9.6 and ROOT 5.34
Realistic input distributions based on LISE++ calculations
Different geometries available
Information of the track of all particles inside the gas stored in a ROOT file
http://geant4.web.cern.ch/geant4/
http://root.cern.ch
http://lise.nscl.msu.edu/lise.html

## Slide 10: Event generation
Two step simulations: Implantation+Decay
Initial beam properties calculated with LISE++ and inserted in GEANT
Decay: Initial position distribution from Implantation stage
Radioactive Beam
Gas Volume
Gas Volume
Implant
Decay
ne
b
p

## Slide 11: Simulation of drift, amplification and digitization of MPGDs
  Calculation of primary electrons from energy deposited at each interaction step with Poisson fluctuation.
  Randomization of the final position at the anode according to transversal diffusion coefficients for each of the electrons produced (Charge spread)
  Gain fluctuations calculated for each electron using the Polya distribution.
  Charge collected on pads is the sum of all the electrons produced.
  Charge threshold applied.
(x1,y1,z1,t1,DE1)

## Slide 12: Considered Geometries
Box-shaped detector
120x120x180 mm
X and Y lengths defined to fit inside SeGA ring
Segmented rectangular pad plane (20x40 mm) parallel to the beam axis
Cylindrical detector
 180 mm x 200 mm length
Keeps the symmetry of SeGA array rings
Central pad ( 60 mm) + 4 sectors (120 mm), perpendicular to the beam axis

## Slide 13: Box Geometry
p
b
Beta contribution lower than 150 keV
Resolution 7% FWHM at 200 keV
All
Protons
Betas
23Al b-delayed proton emission

## Slide 14: Cylindrical Geometry
b
p
Beta contribution lower than 150 keV
Resolution 6.5% FWHM at 200 keV
All
Protons
Betas
23Al b-delayed proton emission

## Slide 15: Summary and Outlook
Simulation operative and running
Beta background as low as 150 keV for both geometries
Next Steps:
  Define final geometry by end of summer to order the MicroMEGAS to CERN
  Investigate position sensitive pad planes for multi particle emission
  Add gamma detectors to simulation
  Test with MicroMEGAS prototypes
  Commissioning experiment with 23Al beam

## Slide 16: Thank you for your attention!